Pitch or roll over? Fixed wing aircraft turn and pitch dynamics

# Introduction

# Basics

In level flight, lift generated by the wing equals mass* gravity

Drawing 1: Level flight

When banked in a moderate balanced turn, more lift needs to be generated by the wing. A component of the wing lift is directed sideways which accelerates the aircraft around the turn.

In a flat turn, the elevator mostly influences the earth based pitch and not the earth based rotation. Rolling the aircraft slightly does not greatly influence the turn rate or pitch rate.

Drawing 2: Flat turn

During a moderate turn, roll angle and elevator control contributes to both pitch and yaw. Rudder also contributes to both. In a normal co-ordinated turn, rudder needs to be applied to avoid slip which increases drag. The ideal turn has no component of acceleration in the span axis of the aircraft.

Drawing 3: Moderate turn

In a steep balanced turn the lift generated by the wing is much larger than the lift required against gravity. Elevator has very little influence on earth based pitch. Most aircraft do not have enough control authority on the rudder to change pitch. Using the rudder and body lift to influence pitch causes more drag than using lift wing so it should be avoided.

Drawing 4: Steep turn

To control pitch, the aircraft must roll slightly to change the direction of the lift it is generating. The result is an increase/decrease of pitch but a corresponding decrease/increase of turn rate. To keep a constant turn rate, the lift force (elevator) must be changed.

Drawing 5: Altered roll angle for pitch control

This leads to some questions:
- What happens when the limits of lift are reached, either by maximum airframe stress or by stall limit?
- Should turn rate be kept constant as the roll position is modified?
- Some aggressive turns demand that that the aircraft turns through inverted. What happens when the aircraft is inverted?
- If the aircraft is moved from desired roll position by turbulence or control error, what should the response be?
- What happens when the aircraft is at a moderate to steep pitch angle.
# Mathematical description

## Balanced co-ordinated turn in level flight
Calculating the expected pitch and yaw rates in a balanced and co-ordinated turn. Input is the roll angle to vertical.

In a balanced turn where there is zero earth pitch:

Where:
Fg = force due to gravity
Drawing 6: Forces in a balanced co-ordinated turn

Fg=m*g
Ft=m*g*tanF
Fl=m*g/cosF
F
Fl = Lifting force
Ft = Resulting tangential force from lift

There will also be a small force from the rudder in a co-ordinated turn but that will be dismissed for now.

The tangential force causes acceleration around a turn. The acceleration is:
V''t = Ft / m = g*tanF

and the earth based vertical axis rotation rate is:

γ' = V''t / Vf
where:
Vf is forward velocity
γ' is the rate of earth heading change

This turn is a rotation which will be measured by both pitch and yaw gyros in varying ratio depending on the roll angle.

q = γ' * sinF
r = γ' * cosF
where q is aircraft pitch rate and r is the aircraft yaw rate.
## Balanced co-ordinated turn during pitch adjustment
In this case, the aircraft rotates away from its balanced turn to make a pitch adjustment. Inputs are the required turn rate and the required pitch rate.

Drawing 7: Forces during pitch adjustment

Ft
Fln
Fla
Fpa

# Definitions
Forces and Moments
Quantity	Variable	Dimensionless Coefficient	Positive Direction
Lift	L	CL = L/qS	'Up' normal to freestream
Drag	D	CD = D/qS	Downstream
Sideforce	Y	CY = Y/qS	Right, looking forward
Roll	l	Cl = l / qSb	Right wing down
Pitch	M	Cm = M/qSc	Nose up
Yaw	N	Cn = N/qSb	Nose right

Angles and Rates
Quantity	Symbol	Positive Direction
Angle of attack	a	Nose up w.r.t. freestream
Angle of sideslip	b	Nose left
Pitch angle	Q	Nose up
Yaw angle	Y	Nose right
Bank angle	F	Right wing down
Roll rate	p	Right wing down
Pitch rate	q	Nose up
Yaw rate	r	Nose Right
Earth heading	γ	Nose right